## Slide 1: Rural Electrification in Thailand
Lessons Learned from Successful Program
Rural Electrification Workshop, Naypidaw
Myanmar May 30-31 2013
Voravate Tuntivate
Consultant
EASWE, World Bank

## Slide 2: Outline
Background
Rural Electrification Planning Stage and Government Commitment
Institutional Choice to Implement Rural Electrification Program
Financing Rural Electrification Program
Strategies to Maintain Financial Viability

## Slide 3: Background
In the 1970s when Thailand embarked on rural electrification, the total population was about 35 million people
Per capita GDP was about US$2,200
Only about 20 percent of villages were electrified (grid)
By 1996 more than 98% of the villages were electrified and over 90% of the households have access to grid electricity
As of 2011, 73,348 villages or 99.98% of villages were electrified (grid); 98.87 of all households (15,89 million households) have access to grid electricity

## Slide 4: Percentage of Thai Villages with Access to Grid Electricity (1972-2001)
Chart: Pertentage of villages with access to electricity
 | 0.15 | 0.16 | 0.17 | 0.18 | 0.21 | 0.23 | 0.25 | 0.3 | 0.33395 | 0.43029 | 0.51133 | 0.56498 | 0.60518 | 0.6572 | 0.7314 | 0.80488 | 0.83833 | 0.88672 | 0.92742 | 0.95309 | 0.9752 | 0.97614 | 0.97714 | 0.98092 | 0.98363 | 0.98671 | 0.98831 | 0.9895 | 0.98974 | 0.98975

## Slide 5: Division of Responsibilities for Power Sector in Thailand
PEA
(Provincial Electricity Authority)
Distribution to all provincial cities and rural areas outside Bangkok Metro Area (BMA)
MEA
(Metropolitan Electricity Authority)
Distribution to the BMA

## Slide 6: PEA Service Territories
Area coverage 510,000 sq.km or 99.9%of the country
74 provinces
16.02 million customers
901 offices
MEA Service Territories
Bangkok Metro Area
Nonthaburi, and
Samut Prakarn

## Slide 7: Profile of Provincial Electricity Authority (PEA)
115 kV Transmission line 6,702 cct-km
Substation
  115 kV 6 Substations
  115/69 – 33/22/11 kV, 348 Substations
HV Distribution Lines 266,749 cct-km
LV Distribution Lines 391,594 cct-km

## Slide 8: Planning Stage and Government Commitment

## Slide 9: Preliminary Steps of Rural Electrification in Thailand
Planning for RE in Thailand began in 1971
In 1973, the government of Thailand officially approved the feasibility study report and adopted as the National Plan for Accelerated Rural electrification (5 successive 5 years plan)
In 1975, new government took office and decided to accelerate the RE program (plan was compressed to 15 years, with 2 years overlap)
Revised national plan was approved by the Council of minister in 1975 and serve as a blue print for the electrification program in Thailand

## Slide 10: Government Commitment to Rural Electrification and Rural Development
The Government was committed to rural electrification and coordinate rural electrification with other development programs.
National electrification plan and successive rural electrification projects are integrated in the National Economic and Social Development Plan (NESDP), each plan covering a five-year period, is considered the country’s blueprint for development activities

## Slide 11: National Electrification Plan Has the Following Key Features
Estimated magnitude of physical and financial requirements, and time-frame to complete the program;
Criteria for designating priority regions for electrification;
Criteria and concept of priority of village selection;
Organization and management requirements;
Analytical parameters for system planning;
Technical standards;
Load promotion program;
Electricity pricing; and
Rural electrification construction, operation and maintenance procedures.

## Slide 12: Institutional Choices to Implement Rural Electrification in Thailand

## Slide 13: Institutional Choices and Decision to Maintain Existing Institutional Arrangement
Splitting PEA into several distribution companies to implement RE would requires several team of capable engineers and technicians, PEA did not have enough engineers and technicians
Need sufficiently large service territories to provide cross subsidy from large and urban to rural customers; with subsidies PEA can maintain some financial independent for RE operation and investment

## Slide 14: Institutional Choices: Problem Solving
PEA has clear national mandate to provide electricity to provincial cities and rural areas throughout the country
Free to concentrate solely on distribution (PEA also has a special office (ORE) for RE projects
Do not have to concern itself with power generation, transmission, and provide electricity services to high demand and high growth area
PEA has large customer bases including both urban, rural, commercial and industrial customers
Large and urban customers cross subsidize rural customers

## Slide 15: Financing Rural Electrification

## Slide 16: How did Thailand Finance rural electrification program?
System of cross subsidies and Uniform national tariffs
Blending of grants, concessional and commercial loans
Mandate to maintain financial viability

## Slide 17: Uniform Electricity Pricing Policy and Cross Subsidies
Both PEA and MEA were required to use the same electricity retail rate structures
Electric retail tariff rate structures were designed to charge larger users at higher rate than small users (large customers to rural households)
EGAT was required to charge PEA at 30 percent lower than it charges MEA (BMA customers to provincial customers)
Government pricing policy provided a reasonable return on investments and sufficient funds to finance the expansion program of each power company

## Slide 18: Example: Thailand’s Rate Structure, Circa 1992 (Residential)
Exchange Rate 25 Baht = 1 US$,
Up to 35 kWh cost 4.8 US Cents or 1.20 Baht per kWh
Notes: The first 5 kWh is 5 Baht (we consider it a fixed charge)
151 to 400 kWh at 8.9 US cents or 2.25 Baht per kWh
>400 kWh at 10 US cents or 2.50 baht per kWh

## Slide 19: Example: Thailand’s Rate Structure, Circa 2002 (Residential)
Fixed charge of US$0.20 cents or 8 Baht for <150 KWh
Fixed charge of US$1.02 or 40.80 Baht for >150 KWh
Exchange Rate 40 Baht = 1 US$
Chart: Monthly kWh blocks
 | 3.394 | 3.394 | 3.394 | 3.8613 | 3.8613 | 4.492 | 4.492 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.45 | 5.6835 | 5.6835 | 5.6835 | 5.6835 | 5.6835 | 5.6835 | 5.6835 | 5.6835 | 5.6835 | 5.6835 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 6.9452 | 7.445 | 7.445 | 7.445 | 7.445 | 7.445
Notes: Fixed charged here is 8 Baht, large residential users pay 2.78 and 2.98 Baht/kwh

## Slide 20: Example: Thailand’s Rate Structure, Circa 2013 (Residential)
Fixed charge of US$0.27 cents or 8.19 Baht for <150 KWh
Fixed charge of US$1.28 or 38.22 baht for >150 KWh
Exchange Rate 29.8 Baht = 1 US$
Chart: Monthly kWh blocks
 | 6.2523 | 6.2523 | 6.2523 | 8.398 | 8.398 | 9.2446 | 9.2446 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.5305 | 10.844 | 10.844 | 10.844 | 10.844 | 10.844 | 10.844 | 10.844 | 10.844 | 10.844 | 10.844 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 12.5376 | 13.2084 | 13.2084 | 13.2084 | 13.2084 | 13.2084
Notes: Fixed charge is 8.19 Baht for < 150 kWh/mo
Fixed charge is 38.22 Baht for > 150 kWh/mo

## Slide 21: Effect of Bulk Rate Concession
The 30% lower bulk rate has resulted in significant cost savings for PEA, because virtually 100% of electricity are bought from EGAT
The savings have helped alleviate problems of high operating costs, combined with the fact that PEA could not charge higher rate for its rural customers, the savings have also helped finance RE program
Enable PEA to keep electricity price for rural customers at affordable level

## Slide 22: Blending of Grants, Commercial, and Concessional Loans
From the 1970s through the mid-1980s Thailand’s government had limited ability to fund RE, so PEA sought grants and concessional loans from bilateral and multilateral development agencies
From 1976 to 2000 PEA obtained about 20 grants and concessional loans to finance RE projects

## Slide 23: Strategies to Maintain Financial Viability

## Slide 24: How did PEA manage to maintain financial viability?
Keeping RE investment cost low,
Minimize operating costs
Maximize revenue
Committed to customer services and actively work to reduce losses (technical and non technical)
Emphasize cost recovery

## Slide 25: Strategies to Contain/Minimize Capital Investment
Blending concessional with commercial loan
Standardization of system design and various components to keep costs low
Bulk purchase of equipment & components
When possible PEA relied on locally made or assemble equipment and components to reduce costs
Use systematic model for planning and sound village selection to manage and minimize investment costs
Voluntary system of contributions for the capital costs of extension

## Slide 26: Technical Standards: Standardization
PEA standardized the system, designs, materials, and construction techniques to reduce and control construction costs and applied to all RE projects
After consulting with the generation and transmission company (EGAT), PEA’s engineers finally decided to select 33 kV and 22 kV as the standard for its distribution system throughout the country
Standardization made the tasks of rural electrification field engineers and construction crews easier to do, field engineers only check operation manual

## Slide 27: Systematic Model for Planning and Sound Village Selection
Uses sound methods for village extension priority, the methods give priority to villages:
  With potential for high demand load
  Large productive uses of electricity
  Maximum achievable economic return, and
  Least cost optimization for grid connection
Quota of villages allocation must maximize economic impacts at the same time minimize implementation costs
Enable the government to integrate RE with other development plan
Carry out detailed feasibility study for every individual project

## Slide 28: Find Solution to Mitigate Political Interference
Provide flexible alternatives for those--including politicians--who wanted to have electricity connected at their request (RE extension consisted of 3 schemes)
  standard village selection and prioritization criteria
  villages which could afford to pay at least 30 percent of the construction costs (will be connected sooner than normal)
  Villages willing to pay the full construction costs (immediate connection)
Give due regard to social and politically unstable area

## Slide 29: Strategies to Contain/Minimize Operating Cost
Cost recovery is priority (PEA’s village selection and prioritization scheme was designed to maintain its cost-recovering and maximize the economic and financial return on its investment).
Low cost and efficient bill collection methods
  PEA hired a respected local person (e.g. school teacher, village head, or village elder) to collect bills in the village

## Slide 30: Actively Engage in Marketing and Load Promotion
  Promote rice mill owners to convert from diesel to electric motor, and
  Promote new rice mill owners to use electric motor
  PEA worked with Bank of Agriculture and Agriculture Cooperative (BAAC) to provide loan to interested rice mill owners for investing in electric motor
  Allow rice mill owner to pay connection fee (without interest) in 12 equal monthly payment

## Slide 31: Committed to Customer Services and Actively Work to Reduce Losses
PEA adopted specific performance measures and practices to ensure high-quality and responsive service
Setting target to increase the number
  Connections
  Service interruptions
  System losses (non-technical and technical)

## Slide 32: Maximize High Connection Rate
Engage with local community and actively promote connection
Low connection fee to increase connection rate
  Provide credit to home owner for house wiring
Commitment to services and affordability
Electricity tariffs structure has life-line rate to assist poor households or low electricity users
Implement system of cross-price subsidies to keep electricity tariff at affordable level for everyone

## Slide 33: Life Line Rate to Keep Tariffs Affordable Thailand
 | Price in Baht per kWh |  | 
 | 1992 | 2002 | 2013
Fixed Charge | 5.00 | 8.00 | 8.19
0 to 5 | 0.00 | 0 | 
6 to 15 kWh | 0.70 | 1.36 | 
0 to 15 kWh | N/A | N/A | 1.86
16 to 25 kWh | 0.95 | 1.54 | 2.50
26 to 35 kWh | 1.20 | 1.80 | 2.75
Monthly Bill in Baht | 33.50 | 54.99 | 88.71
in US$ | 1.34 | 1.37 | 2.98
Avg Effective rate per kWh in Baht | 0.96 | 1.57 | 2.53
in US$ | 0.038 | 0.039 | 0.084
Exchange rate per one US$ | 25.00 | 40.00 | 29.80

## Slide 34: Conclusion
Commitment to financial soundness
Careful planning for system expansion including sound methods of village selection
Diligent attention to keeping costs low
Ensuring revenue collection
  Unique billing program
  Pay attention to services and customers
  Marketing and load promotion
System of cross subsidies that help PEA serves high-cost rural customers at reasonable price
Avoid political interference
Dedicated distribution company
Seeking strong local support

## Slide 35
Thank You